## Slide 1: Access Control Lists. Network Address Translation
Module 3
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Questions
sli.do #NetAdvanced

## Slide 3: Table of Contents
Access control lists overview
Access control lists configuration
  Creating ACLs
  Assigning ACLs
Network address translation
Demonstration

## Slide 4
Access control lists overview

## Slide 5: What is an ACL?
ACL: Access Control List
ACL is a list of rules – each of them is permit or deny
Created and applied on a Layer 3 device
A device with applied ACL acts like a firewall

## Slide 6: Why to implement ACLs?
ACLs filter the network traffic
  Better security
  Can increase the overall network performance
ACLs may just select traffic for other reasons:
  Applying QoS
  NAT
  Traffic mirroring

## Slide 7: ACL types
Standard ACLs – can filter only the source IP address of a packet
    Extended ACLs – can filter based on:
    Source and/or destination IP address
    Source and/or port TCP/UDP number
    IP protocol (DNS, FTP, HTTP, etc.)
    Ethernet frame header ACLs
    Filtering based on source or destination MAC address
    Not very common

## Slide 8: ACL process order
Is there a match?
Test the packet against criteria in 1st rule
Perform action: permit OR deny
End
Yes
Test the packet against criteria in 2nd rule
Is there a match?
No
End
Yes
Perform action: permit OR deny
Test the packet against criteria in Nth rule
No
Is there a match?
Perform action: permit OR deny
End
Packet is denied
End
Yes
No

## Slide 9: Questions
sli.do #NetAdvanced

## Slide 10
Access Control Lists configuration

## Slide 11
Access Control Lists configuration
Creating ACLs

## Slide 12: Standard ACLs configuration
ip access-list standard [<1-99> or name]
[permit or deny] network [wildcard mask ] or any or host
Examples:
  ip access-list standard test_standard
    permit 192.168.1.0 0.0.0.255 (the whole 192.168.1.X network)
    deny host 10.1.1.1 (only the host with IP 10.1.1.1 matches here)
    deny host 172.16.34.15 (the exact 172.16.34.15 host)
    permit any (anything else which did not match before)
    deny any (do not forget the implicit deny at the end of each ACL!)

## Slide 13: ACL process order – example 1 with standard ACL
deny host 10.1.1.100
(deny any)
Q: Is Laptop1 allowed to reach Server1?
  A: No
Q: Is Laptop2 allowed to reach Server1?
  A: No
*An ACL must also be applied to an interface, this is discussed in the next section

## Slide 14: ACL process order – example 2 with standard ACL
deny host 10.1.1.100
permit host 10.1.1.200
(deny any)
Q: Is Laptop1 allowed to reach Server1?
  A: No
Q: Is Laptop2 allowed to reach Server1?
  A: Yes

## Slide 15: ACL process order – example 3 with standard ACL
(deny any)
Q: Is Laptop1 allowed to reach Server1?
  A: No
Q: Is Laptop2 allowed to reach Server1?
  A: Yes
deny host 10.1.1.100
permit 10.1.1.0 0.0.0.255

## Slide 16: ACL process order – example 4 with standard ACL
(deny any)
Q: Is Laptop1 allowed to reach Server1?
  A: Yes
Q: Is Laptop2 allowed to reach Server1?
  A: Yes
permit 10.1.1.0 0.0.0.255
deny host 10.1.1.100

## Slide 17: ACL process order – example 5 with standard ACL
(deny any)
Q: Is Laptop1 allowed to reach Server1?
  A: No
Q: Is Laptop2 allowed to reach Server1?
  A: No
permit 10.1.2.0 0.0.0.255

## Slide 18: ACL process order – example 6 with standard ACL
(deny any)
Q: Is Laptop1 allowed to reach Server1?
  A: Yes
Q: Is Laptop2 allowed to reach Server1?
  A: Yes
deny 15.1.2.0 0.0.0.255
permit any any

## Slide 19: Extended ACLs configuration
ip access-list extended [<100-199> or name]
[permit or deny] protocol [source] network or any or host [destination] network or any or host
Examples:
  ip access-list extended test_extended
    deny ip host 10.1.1.1 host 20.2.2.2
    permit tcp 10.12.12.0 0.0.0.255 host 20.2.2.2 eq www
    deny icmp any 172.16.0.0 0.0.255.255 echo
    deny ip any any (do not forget the implicit deny at the end of each ACL)

## Slide 20: ACL process order – example 1 with extended ACL
Q: Is Laptop1 allowed to reach Server1?
  A: Yes
Q: Is Laptop2 allowed to reach Server1?
  A: No
deny ip host 10.1.1.200 host 192.168.1.100
permit ip any any
(deny ip any any)

## Slide 21: ACL process order – example 2 with extended ACL
Q: Is Laptop1 allowed to reach a web page on Server1?
  A: Yes
Q: Can Laptop1 ping Server1?
  A: No
Q: Is Laptop1 allowed to reach Telnet and FTP on Server1?
  A: No
deny ip host 10.1.1.200 host 192.168.1.100
permit tcp host 10.1.1.100 host 192.168.1.100 eq 80
(deny ip any any)

## Slide 22
Access Control Lists configuration
Assigning ACLs

## Slide 23: Assigning ACLs
An ACL in the configuration has zero effect if it is not assigned to interface
ACLs can be assigned to interfaces inbound or outbound

## Slide 24: Assigning ACLs - inbound
ACL is assigned for inbound traffic

## Slide 25: Assigning ACLs - outbound
ACL is assigned for outbound traffic

## Slide 26: Assigning ACLs – best practices
deny HTTP only from Laptop1

## Slide 27: Assigning ACLs – best practice for standard ACLs
deny HTTP only from Laptop1

## Slide 28: Assigning ACLs – best practice for extended ACLs
deny HTTP only from Laptop1

## Slide 29: Questions
sli.do #NetAdvanced

## Slide 30
Network address translation

## Slide 31: What is NAT?
NAT: Network Address Translation
Used to change the source and/or destination IP address of the packets

## Slide 32: Why NAT?
Primary idea – to solve the “not enough IPv4 addresses” problem
There are only ≈ 4 billion addresses (in IPv4) – quite insufficient for the huge number of Internet users
NAT allows the private addresses to be reused since they are not routed in Internet

## Slide 33: Types of NAT
Source NAT
Destination NAT
Bidirectional NAT

## Slide 34: Source NAT (SNAT)
Source: 10.1.1.100
Destination: 212.3.4.5
Source: 84.12.11.3
Destination: 212.3.4.5
SNAT

## Slide 35: Destination NAT (DNAT)
DNAT
Source: 212.3.4.5
Destination: 10.1.1.100
Source: 212.3.4.5
Destination: 84.12.11.3

## Slide 36: Bidirectional NAT
Source: 10.1.1.100
Source: 84.12.11.3
SNAT
DNAT
Destination: 10.1.1.100
Destination: 84.12.11.3

## Slide 37: NAT terminology
Inside local address - assigned to a host on the inside network, typically private IP address
Inside global address - a public, legitimate IP address that represents one or more inside local addresses to the outside world
Outside local address - IP address of an outside host as it appears to the inside network (can be private address)
Outside global address – public address assigned to a host on the outside network

## Slide 38: NAT vs PAT
PAT: Port Address Translation
In NAT, 1 private address is translated to 1 public address
In PAT, multiple private addresses are translated to 1 public
PAT creates a table which matches: Inside local:source_port -> Inside global:unique_source_port
This way PAT knows to which exact internal host should forward the returning traffic

## Slide 39: PAT – example 1
Inside local | Inside global | Outside local | Outside global
10.1.1.100:1024 | 84.12.11.3:1024 | 212.3.4.5:80 | 212.3.4.5:80
10.1.1.200:1025 | 84.12.11.3:1025 | 212.3.4.5:80 | 212.3.4.5:80

## Slide 40: PAT – example 2
Inside local | Inside global | Outside local | Outside global
10.1.1.100:1024 | 84.12.11.3:1024 | 212.3.4.5:80 | 212.3.4.5:80
10.1.1.200:1024 | 84.12.11.3:1025 | 212.3.4.5:80 | 212.3.4.5:80

## Slide 41: NAT configuration – define the interfaces
ip nat inside
ip nat outside

## Slide 42: NAT configuration – define the translations
ip nat inside source list command:
  translates the source of IP packets that are traveling inside to outside
  translates the destination of the IP packets that are traveling outside to inside
    ip nat outside source list command:
  translates the source of the IP packets that are traveling outside to inside
  translates the destination of the IP packets that are traveling inside to outside
*The first command is used much more often than the second one

## Slide 43: Questions
sli.do #NetAdvanced

## Slide 44
Demonstration

## Slide 46: Summary
…
…
…
Access control lists overview
Access control lists configuration
  Creating ACLs
  Assigning ACLs
Network address translation
Demonstration

## Slide 48: СофтУни диамантени партньори

## Slide 49: СофтУни диамантени партньори

## Slide 50: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg
Software University Foundation
  http://softuni.foundation/
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg