## Slide 1: Network Access, Security and VLANs
Module 3
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Questions
sli.do #NetFund

## Slide 3: Table of Contents
Device memory components
Accessing network devices
Securing network device access
Introduction to VLANs
VLAN details
Demo

## Slide 4
Device memory components

## Slide 5: Main memory components in a network device
RAM (Random Access Memory )
    stores the running configuration file
    loses content when the power goes down
NVRAM (NonVolatile RAM)
    stores the startup configuration file
    retains content when the power goes down

## Slide 6: Main memory components in a network device (2)
Flash memory
  stores the device image (operating system)
  retains content when the power goes down
ROM (Read-Only Memory)
  maintains instructions for power-on self test (POST) diagnostics
  Stores bootstrap program and basic operating system software
  retains content when the power goes down

## Slide 7: Saving the configuration
The configuration file must be saved to survive reboot
To save the running configuration file (stored in RAM) to the startup configuration file (stored in NVRAM), use either:
    copy run start
    write memory
running config
startup config
configuration
changes

## Slide 8: Loading the configuration
The saved configuration file (startup config file) will go in the RAM (the running config file) when:
  the device is restarted
  a copy start run command is executed
running config
startup config

## Slide 9: Questions
sli.do #NetFund

## Slide 10
Accessing network devices

## Slide 11: Out-of-band vs in-band management
Out-of-band:
    Management traffic uses separate path from the user traffic
    Typical protocol: Console
In-band management
    Management traffic travels the same path as user traffic
    Typical protocols: Telnet, SSH, SNMP, Web

## Slide 12: Out-of-band management
Dedicated channel for management only
Needs terminal emulator software (Putty, SecureCRT, etc.)
No IP addresses are required
More secure & reliable for management
Traffic is local and not routed

## Slide 13: Out-of-band management (2)
Typical default configuration for a terminal emulator
Consult the device documentation if not using the defaults

## Slide 14: In-band management
Management session on top of existing data connection
Needs L3 connectivity – IP addresses are required
More convenient to use but not always secure and reliable

## Slide 15: Telnet
Common protocol for managing networking devices
Works on TCP port 23 (by default)
Low security – does not provide encryption
Easy to configure and use

## Slide 16: SSH (Secure Shell)
SSH (Secure Shell) – the secure alternative of Telnet
Uses public-key cryptography to authenticate the remote computer
Works on TCP port 22 (by default)
A bit more difficult to setup

## Slide 17: SNMP overview
SNMP - Simple Network Management Protocol
Used to collect data about managed devices on an IP network
Can also be used to push configurations to the devices
A lot of Network Management Systems use SNMP as their underlying protocol

## Slide 18: SNMP Versions
SNMP v1
    poor security
    not very good performance
SNMP v2c
    poor security
    better performance
SNMP v3
    Secure and with good performance
    More difficult to configure

## Slide 19: Questions
sli.do #NetFund

## Slide 20
Securing network device access

## Slide 21: Where to apply device access security?
Physical security (often underestimated)
Set passwords and privileges
Implement ACLs (will be discussed in the advanced course)
NOTE: Different vendors use different methods for setting and resetting passwords. The next slides will focus on some general Cisco concepts

## Slide 22: The enable password/secret
The password to protect the privilege exec mode (privilege level 15)
Can be set with either:
  enable password
  enable secret
  Recommended to use enable secret for better security

## Slide 23: Interfaces to protect
Two important interfaces to be protected:
    Line Console 0 – the console access (out-of-band)
    Line VTY 0 N* – the Telnet and/or SSH access connections (in-band)
*N depends on the OS, usually is 15 or 63

## Slide 24: Authentication methods
Each interface (console or VTY) can be configured to:
    Does not ask for a password: no login
    Asks for password: login
    Asks for a username and password: login local (Local accounts must exist to support it)
* These are Non-AAA Authentication methods

## Slide 25: Privilege levels
Two default privilege levels are configured:
  privilege 1 - this is the user exec mode >
  privilege 15 - this is the privileged exec mode #
  You can also define custom levels numbered from 2 to 14 and:
  Associate each level with allowed commands (use the privilege command)
  Assign a password to level n (enable secret level n password)

## Slide 26: Privilege levels (2)
To check your current privilege level, use show privilege
To change your privilege level to n, use enable n

## Slide 27: Encrypting all passwords
To encrypt all passwords in the configuration, use service password-encryption

## Slide 28: Password reset
Lost or forgotten passwords can be reset if you have local access to the device, typically with console connection
A password is not recovered meaning that you typically can not find the lost one
Instead, you specify a new password (or delete the old one)

## Slide 29: Password reset procedure
Enter into the emergency (rommon) mode
Instruct the device to bypass its config file (set the configuration register to 0x2142)
Load the device without configuration
Make “copy start run”
Delete or set a new password
Save the config
Set the configuration register back to 0x2102
Reboot

## Slide 30: Secure Access - best practices
Physically secure the devices
Use SSH instead of Telnet
Use SNMPv3 instead of v1 or v2
Use HTTPS instead of HTTP
Out-of-band management (console) is considered more secure than in-band management
Create strong passwords for each privilege level and method of access (console, VTY)

## Slide 31: Questions
sli.do #NetFund

## Slide 32
Introduction to VLANs

## Slide 33: A network without (V)LANs
A single LAN with many computers have some drawbacks:
  Low performance - bigger broadcast domain means less efficient utilization of the links
  Bad security - each user can configure an IP address from the same network and there is no L2 isolation

## Slide 34: Multiple LANs separated with a router
A router may connect multiple LANs, which provides:
  better performance (multiple broadcast domains)
  better security (controlled by the router)

## Slide 35: VLANs: Virtual LANs
Logical division of computer networks
One VLAN = One broadcast domain
One VLAN = One IP subnet

## Slide 36: The benefits of the VLANs
Better performance (multiple broadcast domains)
Better security - no connection between the VLANs (unless a L3 device is configured to do this)
Flexibility - regardless of a user’s location, he/she can belong to any VLAN configured by administrator

## Slide 37: Access (untagged) ports
Used to connect to end-user devices
Can be associated with only one VLAN
Uses the “normal” ethernet frame where there is no VLAN information - no VLAN tag

## Slide 38: Trunk (tagged) ports
Used to connect between switches
Can carry information from/to multiple VLANs
Uses the 802.1Q tagged frame

## Slide 39: Tagging between switches
Untagged
VLAN 1
Untagged

## Slide 40: Tagging between switches
Untagged
VLAN 1
Untagged

## Slide 41: Questions
sli.do #NetFund

## Slide 42
VLAN details

## Slide 43: VLANs: defaults and rules
By default, there is only VLAN 1 in each switch
By default, ALL ports belong to VLAN 1 untagged (access ports)
VLAN 1 can not be deleted
Each port must be member of at least one VLAN
Untagged port can belong to only one VLAN at a time
Trunk ports can belong to multiple VLANs at the same time (tagged)

## Slide 44: Trunk port details
Uses IEEE 802.1Q tag to identify each frame
A trunk carries multiple tagged VLANs and (maximum) one untagged VLAN
The untagged VLAN on a trunk is called:
    Native VLAN (Cisco)
    PVID (HPE Comware)
    Untagged VLAN (HPE Provision)

## Slide 45: Trunk port details (2)
When a port is configured as a trunk port, different vendors may have different default behavior:
  All VLANs are automatically allowed on the trunk - Cisco
  None of the VLANs (except VLAN 1) are auto-allowed on the trunk - HPE Comware
The configuration can be changed to overwrite the default behavior depending on your needs

## Slide 46: Common VLAN terms
Default VLAN - all ports belong there by default
Data VLAN - for the end users
Native VLAN (PVID) - untagged
Management VLAN - type of out-of-band management
Voice VLAN - typically has higher priority
Private VLAN - a.k.a. port isolation

## Slide 47: Types of VLANs
Port based VLANs
MAC address based VLANs
IP subnet based VLANs
Protocol based VLANs
Others

## Slide 48: Example: MAC address based VLANs
The Switch will put the frames from the IP-phone in VLAN 100 and the frames from the PC in VLAN 200
How? By reading the frame’s source MAC Address
untagged link
VLAN 100
VLAN 200

## Slide 49: Inter-VLAN routing
Traffic is transferred from one VLAN to another via routing
Layer 3 device with IP address in each VLAN is required
Do I have Layer 3 support on my switch?
    Cisco – L3 default state depends on the device
    HPE Comware - L3 is always on
    HPE Provision - need to manually turn on the ip routing

## Slide 50: Questions
sli.do #NetFund

## Slide 51
Demonstration

## Slide 52: Summary
…
…
…
Device Memory Components
Accessing Network Devices
Securing Network Device Access
Intro to VLANs
VLAN Details

## Slide 54: СофтУни диамантени партньори

## Slide 55: СофтУни диамантени партньори

## Slide 56: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg
Software University Foundation
  http://softuni.foundation/
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg