## Slide 1: Dynamic routing with OSPF
Module 6
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Questions
sli.do #NetFund

## Slide 3: Table of Contents
Introduction to dynamic routing
OSPF introduction
Single area OSPF configuration

## Slide 4
Introduction to dynamic routing

## Slide 5: Static vs dynamic routing
Static routing:
    Routes to destination networks configured manually
    Routing tables not updated if there is better route or lost network
    Big administrative overhead, hard to manage
    Dynamic routing:
    Routers dynamically exchange the networks they know about
    Routing tables are created with the best routes to destinations
    Routing tables dynamically create or remove entries

## Slide 6: Distance-vector vs link-state protocols
    Distance-vector protocols
    Designed for small networks
    Not scalable
    Examples: RIP, IGRP, BGP
    Link-state protocols
    Designed for small, medium and large networks
    Can scale
    Examples: OSPF, IS-IS

## Slide 7: Distance-vector vs link-state protocols (2)
Distance-vector protocols
Link-state protocols

## Slide 8: RIP vs OSPF
RIP: Routing Information Protocol
        not efficient in the communication (uses broadcast, sends only periodic updates in v1)
        classful protocol (by default)
        Uses hop count as a metric
    OSPF: Open Shortest Path First
        very efficient (uses multicast, sends triggered updates)
        classless protocol (but can summarize)
        uses cost as a metric

## Slide 9: RIP Metric: hop count
I will use Router1!
I know how to reach Destination!
I know how to reach Destination!
Note: all routers talk RIP

## Slide 10: OSPF Metric: cost
I will use Router3!
slow links
fast links
I know how to reach Destination!
I know how to reach Destination!
Note: all routers talk OSPF

## Slide 11: Multiple protocols in the same network
?
slow links
fast links
Note: all routers talk RIP and OSPF
RIP: I am better to reach Destination!
OSPF: I am better to reach Destination!

## Slide 12: Administrative distance

## Slide 13: Questions
sli.do #NetFund

## Slide 14
OSPF introduction

## Slide 15: OSPF advantages
Fast convergence with triggered updates
Hierarchical structure (areas)
VLSM support (classless protocol)
Efficient communication with neighbors
Uses intelligent metric (cost)
Open standard

## Slide 16: OSPF disadvantages
Requires more RAM and CPU on the devices – maintains different tables (neighbor, topology, routing)
Requires good and careful design when multiple areas are needed
More complex to configure and troubleshoot

## Slide 17: OSPF terms
LSA – Link State Advertisement
Router ID
Area
ABR – Area Border Router
Autonomous system
ASBR – Autonomous System Boundary Router

## Slide 18: OSPF terms: router ID
I have many names (interfaces), but just call me 2.2.2.2
Hi, 2.2.2.2!
Hi, 2.2.2.2!

## Slide 19: OSPF terms (2)
Autonomous system
ASBR
ABR
ABR
Area 0 = the backbone area

## Slide 20: Wildcard masks
In the subnet masks, 1 means “do care” and 0 means “don’t care”
Examples:
    192.168.1.0 255.255.255.0 -> refers to 192.168.1.0 network
    Loopback address: 10.1.1.1 255.255.255.255 -> exact IP address
    In the wildcard masks, 0 means “do care” and 1 means “don’t care”
    Examples:
    192.168.1.0 0.0.0.255 -> refers to 192.168.1.0 network
    Loopback address: 10.1.1.1 0.0.0.0 -> exact IP address

## Slide 21: Process ID
router ospf process-id
Has a local significance only – the numbers does not have to match between the routers
Separates processes as they are different routing protocols
It is rarely necessary to have more than 1 process on a router

## Slide 22: The “network” command
The network A.B.C.D Wildcard_Mask command makes two things:
  It enables the interface (sends OSPF “Hello” messages)
  It advertises the network (“I know about network A.B.C.D”) to all OSPF enabled interfaces

## Slide 23: The “network” command (2)
R1:
network 10.0.0.0 0.0.0.255
R2:
network 10.0.0.0 0.0.0.255
network 20.0.0.0 0.0.0.255
10.0.0.1
10.0.0.2
20.0.0.1
Hello!
I have network 10!
Hello!
Hello!
…and 20!
I have network 10!
I have network 10 and 20!

## Slide 24: Questions
sli.do #NetFund

## Slide 25
Single area OSPF configuration

## Slide 26: Single area OSPF configuration
Minimum configuration:
  router ospf process_id
  router-id number (optional)
  network A.B.C.D wildcard_mask area number
Example:
  router ospf 1
  router-id 1.1.1.1 (optional)
  network 192.168.1.0 0.0.0.255 area 0
  network 10.0.0.0 0.0.0.255 area 0

## Slide 27: OSPF passive interface
The “network” command advertises the network AND sends hello messages out of the interface
What if there is non-OSPF device on the other end of the link?
    The Hello packets will be useless
    Represents security issues
    One solution: use passive interfaces

## Slide 28: OSPF passive interface (2)
R1:
network 10.0.0.0 0.0.0.255
R2:
network 10.0.0.0 0.0.0.255
network 20.0.0.0 0.0.0.255
10.0.0.1
10.0.0.2
20.0.0.1
Hello!
I have network 10!
Hello!
Hello!
…and 20!
I have network 10!
I have network 10 and 20!
G0/1
passive-interface G0/1

## Slide 29: Useful OSPF commands
show ip ospf interface
show ip ospf neighbor
show run | begin ospf
show ip route [ospf]

## Slide 30: Tracing a route for a packet
Some tips to check which path a packet will take in a multi-path L3 network:
    show ip route – to check a router’s routing table
    tracert A.B.C.D (from Windows)
    traceroute A.B.C.D (from Cisco)
    *Use the Packet Tracer simulation mode
* not applicable in real networks

## Slide 31: Questions
sli.do #NetFund

## Slide 32
Demonstration

## Slide 33: Summary
…
…
…
Introduction to dynamic routing
2. OSPF introduction
3. Single area OSPF configuration

## Slide 35: СофтУни диамантени партньори

## Slide 36: СофтУни диамантени партньори

## Slide 37: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg
Software University Foundation
  http://softuni.foundation/
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg